## Slide 1: Exploring BlueField-2 DPU as an Accelerator for Latency Sensitive Workloads
by
Hamed Seyedroudbari

## Slide 2: About Me
PhD Student at Georgia Tech
  Advisor: Alexandros Daglis
Research Interests
  Datacenters, SmartNICs, Edge Computing
  Optimizing tail latency for latency critical applications
  Why should you care, how does this impact you?
Notes: Bring compute closer to the data.
Now let me explain what tail latency is and maybe this will make a little more sense.

## Slide 3: Inside the Datacenter
Pipeline of microservices
  Very fine grained
  Single-digit µs service times
  Microservices are latency sensitive
  Strict SLOs: care for tail (99th %) latency.
Ad Ranking
Recommendation Systems
Google Query
ML
Database Lookups
Response
Microservice
  Overheads considerably affect service quality.
Notes: Memory hierarchy, storage access, compute, OS scheduler, queueing
Systems built today have to be extremely optimized.
Emulate Microservice and Measure Performance Boost that you would potentially see with DPU as a co-processor.

## Slide 4: BlueField-2 DPU
Network Interface Card
8x Arm Cortex-A72 cores.
  Clocked @ 2.5 GHz
  1MB L2 cache per 2 cores
  6 MB L3 cache
  16GB DDR4
2x 100G port
  100G per port, unidirectional
  200G bidirectional (100G read, 100G write)
Ethernet
BlueField-2 DPU
ConnectX-6
RDMA
Port 1
Port 2
PCIe Switch
Arm Cores
Memory
Host
Server
BlueField-2 DPU

## Slide 5: BlueField-2 DPU Operation Mode
Inline Accelerator
  Bump in the wire
Look-aside Accelerator (Separate Host)
Network
BlueField-2 DPU
Host Server
Cores
Network
BlueField-2 DPU
Host Server
Cores

## Slide 6: System Requirements
High Throughput & Message Rate
Low Latency Data Movement
RDMA Microbenchmark
  Data movement bypasses kernel network stack
  Network stack offloaded onto NIC hardware
  Places message in host’s memory
Client
Memory
Server
Memory
Kernel
Sockets
TCP/UDP
IP
NIC
Kernel Bypass
Application
Socket API
RDMA Verbs API
Notes: Goal of the internship was to push the limits on the Arm cores of the DPU and analyze how much throughput they can sustain and see how they would hold up if they were to process a latency critical workload.
And see if it can be a viable candidate for processing these types of workloads.

## Slide 7: RDMA Microbenchmark
Emulates microservice
n client cores
  n-1 load generating client threads
  1 latency measurement thread
DUT responds with an echo
Load
Generating
Client
Cores
Memory
Cores
Memory
DUT
(i.e. Server, DPU)
Network
Notes: Goal of the internship was to push the limits on the Arm cores of the DPU and analyze how much throughput they can sustain and see how they would hold up if they were to process a latency critical workload.
And see if it can be a viable candidate for processing these types of workloads.
What is the testbed which we run this on

## Slide 8: Testbed Setup
Ethernet
Host Client
Cores
Memory
BlueField-2 DPU
ConnectX-6
RDMA
Port 1
Port 2
PCIe Switch
Arm Cores
Memory
Host Server
Cores
Memory
Load Generator
  What is the max packet rate the BlueField-2 DPU can sustain?

## Slide 9: Client Send Rate
Can client generate enough load to stress DPU?
30.8 M msgs/sec
  Network is not the bottleneck.
  Peak rate supported by the network is 145M msgs/sec.
Ethernet
Host Client
Cores
Memory
BlueField-2 DPU
ConnectX-6
RDMA
Port 1
Port 2
PCIe Switch
Arm Cores
Memory
Host Server
Cores
Memory
Network Path
Notes: 15.4 MRPS * 2 * 86B * 8 = 21.2 Gbps

## Slide 10: Can the DPU’s Arm Cores Keep Up?
BF-2 DPU
  Can DPU keep up with client’s send rate?
20.2 M msgs/sec
  Network is not the bottleneck.
Ethernet
Host Client
Cores
Memory
BlueField-2 DPU
ConnectX-6
RDMA
Port 1
Port 2
PCIe Switch
Arm Cores
Memory
Host Server
Cores
Memory
Network Path
Notes: 10.1 MRPS * 2 * 86B * 8 = 13.9 Gbps

## Slide 11: BF-2 DPU as Message Forwarder
Max Sustainable Throughput
Are we saturating the network?
  9.52 M msgs/sec
Fwd Msg to Server Core (RR Fashion)
2
ingress
egress
Fwd Msg to Origin Client Core
4
Ethernet
Host Client
Cores
Memory
BlueField-2 DPU
ConnectX-6
RDMA
Port 1
Port 2
PCIe Switch
Arm Cores
Memory
Host Server
Cores
Memory
3
Send Msg to DPU Core (RR Fashion)
1
ingress
egress
Recv Msg from DPU Core
5
Network Path
Notes: 4.76 MRPS * 2 * 86B * 8 = 6.5 Gbps

## Slide 12: Putting it all together
BF-2 is the system bottleneck
  Its throughput drops by ½ as a message forwarder.
As an application co-processor it can theoretically boost system throughput by 66%
  Additional compute cores.
SLO
Notes: Memcpy leads to throughput drop
30% is theoretical – describe how you get it.

## Slide 13: Conclusion
BF-2 Arm cores are not apt for real-time data processing at line rate (100G).
Can be a great application co-processor.
Future Work
  Configure/customize DPU Accelerators for line rate processing.
Notes: Uncritical tasks: Route computation, partition discovery, etc.

## Slide 14
Huge thanks to …
  Pavel Shamis (Pasha)
  Luis Peña
  Alexandre Ferreira
  Jon Hermes
  Kurt Lorenzen